## Slide 1: Internship: High Level Synthesis
By Wouter Van Gansbeke
Supervisors: Wim Meeus & Bertrand Dujardin
Notes: Wouter
TODO in een PPT offline versie:
- slidenummers
- grafieken invoegen

## Slide 2: High Level Synthesis: Introduction
Notes: Wouter

## Slide 3: High Level Synthesis: Workflow
Main steps:
Write C / C++ code and test bench
Verify functional behavior of the C / C++ code
Specify top level function, platform, clock, constraints and directives
Synthesize C / C++ to RTL
Verify RTL using the C test bench
Notes: Stijn

## Slide 4: High Level Synthesis: Benefits
Benefits:
Accelerate design time
Reduce verification / simulation effort and time
Easy adaptation to other design requirements (reuse)
Closer to algorithm, less code and by extend less errors
Detect errors early in the design process
Locate bottlenecks fast
=> Productivity increase and time to market decrease!
Notes: Stijn

## Slide 5: High Level Synthesis: Pitfalls
Pitfalls:
No clock accurate designs possible
Some software difficult / impossible to convert to hardware
It is not possible to use existing RTL code as an input for HLS software
Hard to read generated RTL code
Cause of errors not always clear
Maturity of the tool
Notes: Stijn

## Slide 6: From C model to synthesizable C (I)
Code changes:
Top level function cannot be a class member function
C constructs must be of bounded size
  'unsupported memory access on variable'
Pointer to pointer in top level not possible:
  Matrices
  Pointer from within a class to other object
Pointer casting
No recursive functions (tail recursion)
Arbitrary Precision data types to optimize word length
No dynamic memory allocation
No memset, memcopy
Notes: Wouter

## Slide 7: From C model to synthesizable C (II)
Encoutered cosimulation problems:
  'Stuck at TB testing' or 'Segmentation Fault Error' caused by:
    Large chunks of data
    Calling top level functions too much
    Not using volatile pointers when reused
      Amount of rereads/rewrites need to be specified using INTERFACE directive
Solution:
  Array sizing
  Call top-level function a small number of times
  Use Limit diskspace configuration
Notes: Wouter

## Slide 8: Mapping on FPGA
Pointers:
  Can conceal relations
  Limit optimizations
  Monolithic vs Distributed memory on FPGA
  Dynamic memory allocation: stack, heap
Variables in registers
Arrays in block ram
No shared memory but hardware constructs exist
Memory based => stream based on FPGA
Notes: Wouter

## Slide 9: HLS Software: Xilinx Vivado HLS
Positive
Easy & nice Eclipse based GUI
Good tutorial and manual
Online forum
Negative
Bad estimates
File name length limited by default
User responsible for correct cosimulation result
Notes: Stijn
File name limited to 30 characters ==> weird naming of output files and functions, change in solution settings, config_compile, name_max_length

## Slide 10: HLS Software: Mentor Graphics Catapult
Positive
Not limited to Xilinx FPGA's
Good overview of the synthesis steps
Good manuals
Cosimulation: Compares top level I/O of C and RTL code
Negative
Limited amount of shortcuts
Not easy to tweak the result
Too optimistic about critical path
Limited amount of online information
Notes: Stijn

## Slide 11: Arbitrary precision data types
Avoid unnecessary resource utilization
Each vendor different version:
  Vivado HLS : AP (AutoPilot)
  Catapult HLS: AC (Algorithmic C)
Similarly but different:
  Bit padding:
Notes: Stijn

## Slide 12: Optimizations workflow (I)
Directives/ pragma's & config used
Strategy
  Throughput: decrease initiation interval
  Latency
  Area
Notes: Wouter

## Slide 13: Optimizations workflow (II)
1. Initial changes using:
  Interface
    ap_none, ap_memory, ap_vld, ap_ovld
  Datapack
  Loop trip count
  Re-reading
2. Increase concurrency
  Dependencies:
    Dataflow = Read/write
    Anti-dependence = write/read
    Output dependence = write
  Pipeline by decreasing interval (loops)
    Caution: memory accesses when using arrays
    Block RAM has limited ports (2)
    Array partition /array reshape pragma
    Flush pipeline
  Dataflow (functions)
Notes: Wouter

## Slide 14: Optimizations workflow (III)
3. Latency
  Inline recursively: reduce function call overhead
  Latency directive: watch critical path
  For loop incrementation
  Question mark in latency report
4. Area
  Inline
  Adapted datatypes
  Resource directive
  Array mapping
Notes: Wouter

## Slide 15: Report
Notes: Wouter

## Slide 16: Comparison: Design verification time
Original RTL design:
  Compilation: 52 sec
  Running test: 14 min 58 sec
  Total: 15 min 50 sec
Vivado HLS:
  C simulation: 17 sec
  C synthesis: 1 min 44 sec
  C / RTL cosimulation: 2 min 56 sec
  Total: 4 min 57 sec
Catapult C*:
  C simulation: 47 sec
  C synthesis: 3 min 20 sec
  ModelSim simulation: 7 min 20 sec
  Total: 11 min 27 sec
* Catapult running on “beantsu0212” server instead of “devasic”
Chart: VHDL Verification time
| VivHLS | Catapult * | VHDL vsim (original)
compilation | 0 | 0 | 52
C simulation | 17 | 47 | 0
C synthesis | 104 | 200 | 0
VHDL verification | 157 | 440 | 888
Notes: Stijn

## Slide 17: Comparison: Code length
Original RTL design:
  1198 lines in 10 files
  + common files
Vivado HLS generated VHDL:
  3708 lines total in 4 files
Catapult HLS generated VHDL:
  7303 lines in 1 file
C code:
  314 lines main logic
  + common files
Chart: Code length
| LINES
VHDL VivHLS | 3708
VHDL Catapult | 7303
VHDL original | 1198
C Code | 314
Notes: Stijn

## Slide 18: Implementation results
Chart: Implementation results for single_line entity
| Latency | WNS [ns] | WHS [ns] | Power [W] | Temperature [C] | CLB LUT | CLB Reg | Carry 8 | F7 MUX | CLB | LUT as logic | LUT as Mem | LUT FF | Block RAM | DSP
Original | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Vivado HLS | 92.8571 | 89.5238 | 86.5385 | 104.0272 | 100.361 | 102.0214 | 106.6726 | 245 | 100 | 100.2545 | 100.9969 | 119.1874 | 117.0185 | 100 | 95
Catapult C (Timing Violation) | 85.7143 | -73.3333 | 98.0769 | 100.7845 | 100 | 112.6494 | 88.1858 | 352.5 | 100 | 114.4402 | 112.5421 | 114.447 | 101.5116 | 100 | 90
Notes: Stijn

## Slide 19: Problems
No timing closure
  Location:
    Prevent crossing IO gap
    multiple times
  Fanout:
    Signbit drives 52 ports
    = 2*(48-22)
Paths
Stages in mapping on FPGA
  Synthesize
  Place
  Phys opt
  Route
  Post phys opt
Notes: Wouter

## Slide 20: Solutions: Optimize routing methodology
Solve fanout with register replication
  Load is halved, aggressiveFanout directive
Solve location
  Pblock creation
  Ignore DSP in column next to IO block
    DSP48E2_X8Y, DSP48E2_X17Y
Shorten critical path with
  Latency directive
  Resource directive
  Max_fanout directive (only in Catapult)
Notes: Wouter

## Slide 21: Timing Results for complete Bini
WNS : -0.084 ns
TNS : -0.354 ns
12 Failing endpoints
WHS : 0.016 ns
Critical path in bini Ethernet subsystem (single_1g).
No failing endpoints in or connected to the HLS design
Notes: Stijn

## Slide 22: Conclusions
HLS can accelerate RTL design of arithmetic parts a lot
3x faster verification
Reuse of C testbench
4x smaller code to maintain
Easy design changes (i.e. less area, different clock, pipelining ...)
Easy to compare different solutions
Critical path estimates of HLS tools not reliable
Timing critical parts and connecting HLS blocks still needs to be done in RTL
Tools will become better:
  More accurate simulation libraries
  More C code possibilities
Notes: Stijn

## Slide 23: Where to start
Getting started:
This presentation
  Vivado HLS tutorial: chapter 1 & 2
  Mentor HLS Bluebook: chapter 4 – Fundamentals of HLS
Basic reference:
  Vivado HLS reference guide ug902: chapter 3
  Catapult user and reference manual: chapter 8
Notes: Stijn

## Slide 24: Questions?